## Slide 1: Electric Current

## Slide 2: Current Electricity
Current Electricity is the flow of an electric charge through a conductor.
Notes: The flow of electric charges is called electric current (I).
Water current in river

## Slide 3: Direction of Current
Conventional Current:
positive  negative terminal
Electron Flow: We now know it is the electrons that are moving (from negative  positive terminal)
Notes: Initially it was thought that positive charges were moving so movement was always described as from positive to neg terminal.

## Slide 4: Types of Current
Direct Current (DC): electrons travel in only one direction.
Eg. batteries and solar cells,
Alternating Current (AC) results when electrons periodically reverse direction.
Eg Wall outlets in North America reverse current direction 60 times/sec.
Notes: Electric current that flows continuously in a single direction is called a direct current, or DC. In a direct current circuit, current is caused by electrons that all line up and move in one direction.
Within a wire carrying direct current, electrons hop from atom to atom while moving in a single direction. Thus, a given electron that starts its trek at one end of the wire will eventually end up at the other end of the wire.
When the electrons in alternating current switch direction, the direction of current and the voltage of the circuit reverses itself.
The rate at which alternating current reverses direction is called its frequency, expressed in hertz. Thus, standard household current in the United States is 60 Hz.

## Slide 5: Measuring Electric Current (I)
Electric current is the amount of charge passing through a point in a circuit in a given time.
Units: Amperes (A)
1 Amp is the typical amount of current flowing through a lightbulb is.
Notes: Water current in river

## Slide 6: Ammeter measures current
An ammeter is an instrument that measures current at one point in a circuit.

## Slide 7: Reading an Ammeter
An ammeter is connected in series within the circuit.

## Slide 8: Reading an Ammeter
How many Amps?

## Slide 9: Reading an Ammeter
0.3 Amps
Or 300mA

## Slide 10: Calculating Current
Current (I) is expressed by the equation:
Notes: One coulomb is equal to the charge of 6.25 x 10 18 electrons.
One ampere represent the current of one coulomb of charge per second.
Do calc current WS
the quantity of charge is related to the number of electrons flowing past, To make this connection between the current and the number of electrons, one must know the quantity of charge on a single electron.
Qelectron = 1.6 x 10-19 C

## Slide 11: Calculating Current
Q = quantity of charge flowing by a point in a time period of t.
A current of 1 ampere = 1 Coulomb /second.
1 Coulomb is equal to the charge contained in 6.25 x10 18 electrons
1 ampere represents the current of one coulomb of charge per second.
Notes: One coulomb is equal to the charge of 6.25 x 10 18 electrons.
One ampere represent the current of one coulomb of charge per second.
Do calc current WS
the quantity of charge is related to the number of electrons flowing past, To make this connection between the current and the number of electrons, one must know the quantity of charge on a single electron.
Qelectron = 1.6 x 10-19 C

## Slide 12: Calculate how many electrons go past a point in a set amount of time
Q = I x t

## Slide 13: Practice
An ammeter reads 10 A. How many electrons flow through the circuit in 1 min?
Notes: 1 amp = 1 coulomb /sec
10 amps = ?/60 sec
Q = I x t
Q = 10 x 60 sec
Q = 600 coloumbs

## Slide 14: Practice
An ammeter reads 10 A. How many electrons flow through the circuit in 1 min?
First find the number of Coulombs, then convert to electrons.
Remember: 1 C = 6.25 x10 18 electrons
Notes: 1 amp = 1 coulomb /sec
10 amps = ?/60 sec
Q = I x t
Q = 10 x 60 sec
Q = 600 coloumbs

## Slide 15: Practice
An ammeter reads 10 A. How many electrons flow through the circuit in 1 min?
Q = I x t
= 10 A x 60 sec
= 600 C (Coulombs)

## Slide 16: Practice
An ammeter reads 10 A. How many electrons flow through the circuit in 1 min?
Q = I x t
= 10 A x 60 sec
= 600 C (Coulombs)
# electrons = 600C x 6.25 x10 18 electrons/C
= 3.75 x10 21 electrons

## Slide 17: Practice
An ammeter indicates that a current of 1.2 A flow through a lamp. How many electrons will go through the lamp in 45 seconds?

## Slide 18: Practice
I = Q/t
Q= It
Q= (1.2A) (45s)
Q = 54 C
Now convert C to electrons (N)

## Slide 19: Practice
N = 54C ( 6.25 x 10 18 electrons)
1 C
= 3.4 x 10 20 electrons

## Slide 20: Practice Conversions:
525 mA = _____________ A
3.2 mA = _____________ A
4780 mA = ____________ A
2.9 A = _______________mA

## Slide 21: Practice Conversions:
525 mA = 0.525 A
3.2 mA = 0.0032 A
4780 mA = 4.780 A
2.9 A = 2990 mA

## Slide 22: Simple Calculations:
1. A lamp has 5000C of charge flowing through it in 10 minutes. What is the current in the lamp?

## Slide 23: Simple Calculations:
A light has 5000C of charge flowing through it in 10 minutes. What is the current in the light?
I = Q/t
I = 5000C/600 sec
I = 8.33 Amp

## Slide 24: Simple Calculations:
2. An electric heater has a current of 18A. How many hours will it take for 55kC of charge to flow through it?

## Slide 25: Simple Calculations:
2. An electric heater has a current of 18A. How many hours will it take for 55kC of charge to flow through it?
t= Q/I
t= 55 000/18
t = 3055.6 sec = 51 minutes

## Slide 26: Simple Calculations:
3. You hook up an ammeter in a circuit. It reads 4.6A. If you have a bulb hooked up in this circuit, how many electrons will flow through the lamp in 45 seconds?

## Slide 27: Simple Calculations:
3. You hook up an ammeter in a circuit. It reads 4.6A. If you have a bulb hooked up in this circuit, how many electrons will flow through the lamp in 45 seconds?
Q = I x t
Q = 4.6 A x 45
Q = 207 Coulombs, then convert to electrons
N = 207 C x 6.25 x 10 18 electrons = 1294 x 1018
1 C

## Slide 28: Simple Calculations:
4. Your ammeter reads 672mA. If current flows through the circuit for 30 seconds, how many electrons will pass through a bulb during this time?

## Slide 29
4. Your ammeter reads 672mA. If current flows through the circuit for 30 seconds, how many electrons will pass through a bulb during this time?
Q = I x t
Q = 0.672 A x 30 sec
Q = 20.16 C
Electrons = 20.16 C x 6.25 x 10 18 electrons
1C
= 126 x 10 18 electrons

## Slide 30: Getting a shock
Skin is conductive so touching a bare wire completes the circuit and you get a shock.
The severity of the shock depends on the current.
At 0.0001 A (1mA), you will feel a tingling sensation.
At 0.015 A (1.5mA), your muscles will contract
At 1 A (1000 mA), your heart stops.

## Slide 31: Practice
WB page 174 – 175
TRY THIS ACTIVITY p308

## Slide 32: Circuits in Series
only one path for electrons to flow.
Electricity must flow through all devices
If you add electric loads, each one get less electric pressure (light bulbs will dim as more are added)
Notes: All loads in a circuit share the electric pressure (voltage).

## Slide 33: Parallel Circuits
Current splits up
some of the current goes through each device.
None of the current goes through more than one device.

## Slide 34: Series
If you put more lamps into a series circuit, the lamps will be dimmer than before. In a series circuit, if a lamp breaks or a component is disconnected, the circuit is broken and all the components stop working.
Series circuits are useful if you want a warning that one of the components in the circuit has failed. They also use less wiring than parallel circuits.

## Slide 35: Practice
HW: Read p306-308
HW: Answer CYU p 309 # 9, 10,11,13,14,15
HW: WB 10.2 p 174-175
Activity: PHET Simulation, remainder for HW. You will hand this in next class
Notes: Do HO from KL and other WB 10.2, along with reading ammeter